## Slide 1
SIH26025 | Distributed Edge Intelligence for Mine Subsidence Monitoring
AI-Assisted Real-Time Deformation Detection & Early Warning Decision-Support System
System Overview
Surface Sensor Nodes → Wireless Mesh → Pi 4 Edge Gateway → AI/ML Correlation Engine → GIS Dashboard + Alerts
Ministry of Coal / Coal India Limited
Hardware Category | Disaster Management Theme
Objective: Continuous local deformation monitoring between conventional survey cycles
Sensor Layer
ESP32-C3 nodes — tilt, vibration, displacement, crack state
Edge Intelligence
Raspberry Pi 4B — offline-capable AI/ML correlation engine
Output
GIS deformation map, risk zones, SMS/email alerts
Precise framing: This system is an AI-assisted deformation detection and early-warning decision-support tool — not a DGMS-certified structural-safety instrument and not a guaranteed cave-in predictor.

## Slide 2
Problem → Engineering Requirements
Physical Phenomenon Chain
Surface Tilt
Ground Deform
Stress Shift
Extraction
Derived Engineering Requirements
Continuous Monitoring
Distributed sensor nodes — not periodic survey points
Multi-Point Deformation
Wireless surface mesh — spatial correlation across nodes
Local Intelligence
Raspberry Pi edge gateway — inference without cloud dependency
No Reliable Internet
Offline-first architecture — buffer, process, sync on reconnect
False-Positive Reduction
Multi-node spatial correlation — not single-threshold alerting
Low Deployment Cost
ESP32-based nodes — commodity hardware, modular expansion
Core constraint: The system must produce local intelligence and issue alerts even when cloud connectivity disappears entirely.

## Slide 3
End-to-End System Architecture
Four-Layer Distributed Stack
Layer 1 — Sensor Nodes
ESP32-C3/WROOM. Local sampling at configurable intervals. On-node filtering and feature extraction before transmission.
Layer 2 — Mesh Comms
LoRa / Zigbee / Wi-Fi mesh. MQTT telemetry with node ID, timestamp, sequence counter, CRC integrity check.
Layer 3 — Edge Gateway
Pi 4 MQTT broker. Time-series DB. Anomaly detection, multi-node spatial correlation, risk scoring, alert dispatch.
Layer 4 — Application
GIS deformation map, risk zone overlay, operator dashboard, SMS/email alerts, optional cloud sync when online.
Key architectural principle: Intelligence is distributed across the mesh — not centralized in a cloud endpoint. The system degrades gracefully with each layer operating independently if upstream connectivity fails.

## Slide 4
ULTRON Hardware → Mine Monitoring Platform
Existing Infrastructure Mapping
Component | Role in System | Status
Raspberry Pi 4B 8GB | Edge gateway + AI/ML inference + MQTT broker | ✓ Real
Raspberry Pi 3A+ / 3B | Distributed sensor node controllers | ✓ Real
ESP32-C3 / ESP32-WROOM | Sensor interface, relay nodes, edge filtering | ✓ Real
5-Port Ethernet Switch | Local wired backbone for gateway cluster | ✓ Real
500GB SSD | Offline telemetry storage + on-device ML models | ✓ Real
NeoPixel + OLED Display | Visual status indicator + local alert display | ✓ Real
Physical Subsidence Transducers | MPU6050, ADXL345, displacement, crack sensors | Simulated
Prototype Boundary
✓ Implemented & Real
Compute cluster, mesh network, MQTT broker, edge inference engine, correlation logic, GIS dashboard, alert pipeline, SSD storage
⚙ Software-Simulated
Physical subsidence transducers — replaced by sensor simulator publishing identical telemetry over the same MQTT interface
No new compute infrastructure required. Prototype runs entirely on existing ULTRON hardware inventory. Sensor simulator enables hardware-layer substitution without redesigning the downstream stack.

## Slide 5
Sensor & Node Engineering
Physical Deformation → Digital Feature Vector
Node Processing Pipeline
Timestamp & Seq
Extract Features
Apply Filter
Sample Data
Sensor Suite
MPU6050
3-axis tilt / acceleration — primary deformation indicator
ADXL345
High-resolution vibration measurement — seismic event detection
Displacement Transducer
Absolute ground movement — vertical & horizontal components
Crack Sensor
Binary / analog crack-state detection at surface structures
Feature Vector Definition
X(t) = [tilt, vibration_RMS, displacement, crack_state, dX/dt]
Each node publishes a structured feature vector per sample epoch. The derivative term dX/dt encodes rate-of-change, enabling detection of accelerating deformation — the operationally significant condition — not merely absolute displacement magnitude.
Prototype Sensor Status
Software Sensor Simulator
Physical transducers are currently replaced by a deterministic simulator that publishes the identical MQTT telemetry schema — same topics, same packet structure, same QoS levels. The downstream pipeline is sensor-hardware-agnostic by design.
Interface Compatibility
Future hardware sensor integration requires zero modifications to the edge gateway, correlation engine, or application layer. Only the node firmware changes at the physical interface boundary.

## Slide 6
Distributed Telemetry Architecture
Multi-Node Data Pipeline
Mesh Topology & MQTT Topic Tree
mine/node/{id}/data
Routine sensor telemetry — all nodes, configurable publish interval
mine/node/{id}/status
Node health, battery, signal quality, firmware version
mine/gateway/alert
Risk score threshold breach — triggers operator notification pipeline
mine/dashboard/update
GIS map refresh, risk zone overlay, operator dashboard payload
QoS Strategy
QoS 0 — At Most Once
Routine telemetry — acceptable data loss on congestion
QoS 1 — At Least Once
Critical alerts — guaranteed delivery with acknowledgement
Packet Structure
Field | Type | Purpose
node_id | String / UUID | Unique node identity for spatial correlation
timestamp | ISO 8601 UTC | Temporal alignment across mesh
sensor_type | Enum | Tilt / vibration / displacement / crack
value | Float | Calibrated engineering unit reading
unit | String | °, mm/s², mm, boolean
confidence | Float [0–1] | Node self-assessment of reading quality
sequence | Uint32 | Gap detection / replay ordering
CRC | Uint16 | Packet integrity verification
Offline Behavior
Reconnect & Replay
Edge Inference
Buffer Locally

## Slide 7
Anomaly Detection & Mesh Correlation Engine
Intelligence in Space + Time, Not Just Thresholds
Detection Pipeline
Correlation Decision Logic
Case A — Local Disturbance
High local anomaly score + low neighbor correlation → single-node event, likely environmental interference or mechanical vibration. Alert suppressed or downgraded.
Case B — Genuine Subsidence Indicator
Similar temporal deformation pattern across multiple neighbor nodes → spatially coherent ground movement. Risk score elevated. Operator alert dispatched.
Risk Scoring Function
Risk = f(temporal deviation, magnitude, persistence, neighbor correlation)
Score is a weighted composite — a single large spike that is brief and isolated contributes less than a moderate, persistent, spatially-correlated deformation trend. Operator thresholds are configurable per deployment zone.
Detection Methods
Statistical drift detection — CUSUM / EWMA on rolling baselines
Threshold-based alerting — configurable per sensor class
Lightweight ML anomaly detection — on-device inference, Pi 4 GPU-optional
Time-series feature analysis — trend, seasonality, rate-of-change decomposition

## Slide 8
Fault Tolerance, Security & Offline Operation
Designed to Fail Gracefully
Failure Mode Response Matrix
Failure Mode | System Response
Sensor failure | Mark node degraded; substitute neighbor-node readings for correlation
Node failure | Mark node offline; mesh routing continues around failed node
Network loss | Local buffering activated; edge inference and alerts continue uninterrupted
Gateway failure | Distributed node buffering; local NeoPixel/OLED alerts remain active
Time desync | NTP resync on reconnection; sequence numbers maintain ordering integrity
Fail-closed principle: Inability to confirm a safe state generates operator attention — not silence. An unacknowledged alert is treated as a live alert.
Security Architecture
Node Identity
Unique hardware identity per node — prevents spoofed telemetry injection
TLS MQTT
Transport-layer encryption on all broker connections — no plaintext telemetry
Integrity Checks
Sequence counters for gap detection; CRC16 on every packet for corruption detection
Signed OTA
Firmware updates cryptographically signed — prevents unauthorized firmware deployment

## Slide 9
Validation, Testing & Prototype Status
Six-Test Validation Framework
1
Stable Baseline
No deformation input — verify zero false alarms over extended observation window. Pass criterion: alert rate = 0 under quiescent conditions.
2
Single-Node Disturbance
Inject anomaly at one node — verify local detection without mesh-wide alert escalation. Validates correlation logic Case A.
3
Multi-Node Deformation
Simultaneous deformation across nodes A–D — verify spatial correlation triggers elevated risk score and operator alert. Validates Case B.
4
Injected Noise
High-amplitude random noise on sensor streams — verify filtering layer suppresses spurious signals before feature extraction.
5
Network Disconnect
Sever gateway connectivity — verify local buffering, continued edge inference, and correct replay on reconnection.
6
Node Failure
Power-off individual nodes — verify mesh routing adapts, degraded node is marked, and correlation continues on remaining nodes.
Physical Validation Approach
Scale-model ground rig with mechanically actuated deformation — simulated sensor streams injected at calibrated displacement magnitudes. Validates detection pipeline end-to-end.
Case-Study Validation Approach
Public subsidence event data and InSAR satellite deformation datasets used to verify that the correlation and risk-scoring engine would have flagged known events. No accuracy numbers fabricated — validation framework is the deliverable.
Prototype transparency: REAL — compute, network, MQTT, edge inference, correlation engine, GIS dashboard, alert pipeline, SSD storage. SIMULATED — physical subsidence transducers (identical telemetry interface to future hardware).

## Slide 10
Deployment Roadmap & Technical Differentiation
Prototype → Pilot → Scale
Prototype — 3–4 Nodes
ESP32 + Wi-Fi/Ethernet in lab environment. Full stack validated on ULTRON hardware. Sensor simulator in place.
Pilot — 20–50 Nodes
LoRa/Zigbee mesh + ruggedized weatherproof enclosures deployed at mine site perimeter. Hardware transducers integrated.
Scale — 100–1000+ Nodes
Distributed gateway cluster, multi-site synchronization, hierarchical MQTT broker federation, centralized GIS aggregation.
vs. Conventional Mine Monitoring
Dimension | Conventional | This System
Sampling | Periodic survey cycles | Continuous real-time
Coverage | Discrete survey points | Distributed mesh topology
Processing | Central / manual analysis | On-device edge inference
Connectivity | Requires network access | Offline-first, sync on reconnect
False Positives | Single-point thresholds | Multi-node spatial correlation
Alerting | Post-survey reporting | Local + remote, real-time
Scalability | Linear survey cost | Modular node addition
Scope boundary: A distributed, edge-intelligent, offline-capable deformation monitoring layer operating between conventional survey cycles. Decision-support early indicator — not a DGMS-certified structural-safety instrument and not a guaranteed cave-in predictor.