## Slide 1
SIH26178 | AI-Powered Environmental Intelligence Network
Distributed Edge Intelligence for Local, Real-Time Environmental Risk Detection
Organization
Qualcomm Inc. | Category: Hardware | Theme: Disaster Management
MVP Scenario
Forest-fire early indication — edge-first, offline-capable, multi-node
Architecture Pipeline
ESP32 Nodes → Wireless Mesh → Raspberry Pi Gateway → Edge AI → GIS / Alert
Distributed Sensing
ESP32-C3/WROOM nodes with modular sensor interfaces deployed across the monitored environment
Wireless Mesh
LoRa / Zigbee / Wi-Fi mesh with MQTT telemetry — reliable multi-hop packet delivery
Edge AI
TFLite Micro on-node inference plus scikit-learn Bayesian fusion on Raspberry Pi 4B gateway
Alert Integration
SACHET / CAP protocol target — disaster-management authority API integration roadmap
A distributed cyber-physical sensing network designed for continuous local environmental monitoring, autonomous edge processing, and resilient operation during connectivity loss. Complements — does not replace — IMD/ISRO centralized monitoring by providing village/ward-level ground truth between centralized observation cycles.

## Slide 2
From Centralized Monitoring to Local Ground Truth
Engineering Gap
Existing centralized systems provide periodic or sparse observations at regional scale. Local hazards — forest fires, flash floods, air-quality spikes — require minutes-level detection with autonomous decision-making at the point of occurrence. The gap between centralized monitoring cycles is precisely when early-stage hazards escalate unchecked.
Core Requirement
Provide village/ward-level environmental intelligence between centralized monitoring cycles — continuously, autonomously, and without cloud dependency.
Requirement | Conventional Approach | Proposed Distributed Network
Local ground truth | Sparse, point observations | Dense, continuous multi-node sensing
Detection latency | Hours to days | Minutes
Processing location | Centralized cloud / HPC | Edge-first, on-device
Connectivity dependency | Critical — failure = blackout | Offline-capable, local buffering
Deployment cost | High — specialized infrastructure | Low-cost distributed nodes
Hazard coverage | Specialized per-system silos | Common architecture — fire, flood, air, seismic
Alert integration | Separate standalone systems | SACHET/CAP protocol target
Satellite / Centralized
Periodic or sparse regional observations
Delayed Local Awareness
Hours-to-days latency; centralized processing; no offline capability
Gap: Local Hazard Window
Early-stage events escalate between monitoring cycles — undetected at ground level
Proposed: Dense Local Layer
Continuous sensing, edge AI, minutes-level detection, autonomous operation

## Slide 3
End-to-End System Architecture
Layered architecture from field sensors to disaster-management integration. Each layer is independently operational; failure of any upper layer does not silence lower-layer intelligence.
1
Field Sensor Nodes
ESP32-C3 / ESP32-WROOM — smoke, temp, humidity (fire MVP); PM2.5/PM10, gas (air); water level, soil moisture (flood); vibration, pressure (seismic)
2
Local Processing
Sensor sampling & noise filtering; feature extraction (mean, variance, rate-of-change); local anomaly detection; node health monitoring
3
Wireless Mesh
LoRa / Zigbee / Wi-Fi mesh topology; MQTT telemetry; node identity, packet sequencing, CRC checksums; retry logic & local buffering
4
Edge Gateway
Raspberry Pi 4B (8GB) — Mosquitto MQTT broker; data aggregation & multi-sensor fusion; TFLite Micro / scikit-learn inference; SQLite offline store
5
Application Layer
FastAPI backend; GIS dashboard with risk heatmaps; event history & alert management; OLED status & NeoPixel indicators
6
External Integration
SACHET/CAP alert protocol (architectural target); disaster-management authority APIs; buffered synchronization on connectivity restore
Design Invariants
Each layer can operate autonomously if upper layers fail
No raw sensor stream needs to leave the edge network
Only compressed intelligence and alerts propagate upward
All inter-layer communication is authenticated and sequenced
Extensibility by Sensor Configuration
Fire MVP: Smoke + temp + humidity nodes
Flood: Water level + soil moisture + rain
Air Quality: PM2.5/PM10 + gas + temp
Landslide: Vibration + soil moisture + pressure

## Slide 4
ULTRON Hardware → Environmental Intelligence Platform
Repurposing existing ULTRON infrastructure as the physical foundation of the distributed network. No new hardware procurement required for the prototype stage.
Hardware Component | Environmental Network Role | Functional Assignment
Raspberry Pi 4B 8GB | Edge Brain — Central Intelligence | MQTT broker, AI inference, data fusion, persistence, GIS backend
Raspberry Pi 3A+ / 3B | Local Compute Nodes | Distributed processing, mesh relay, redundancy, local buffering
ESP32-C3 / ESP32-WROOM | Field Interface — Sensor Nodes | Sensor acquisition, local filtering, TFLite Micro inference, mesh TX
Ethernet Switch | Local Backbone | Wired intra-cluster connectivity, gateway uplink
Wi-Fi Adapters | Wireless Mesh & Uplink | Wireless mesh participation, external WAN uplink
500 GB SSD | Persistent Storage | Offline data store, model cache, event history, sync buffer
OLED Display | Local Status Indicator | Network health, alert level, node count, last event timestamp
NeoPixel RGB LEDs | Visual Anomaly Indicator | GREEN = nominal / YELLOW = caution / RED = hazard active
GPIO Tripwire | Physical Event Trigger | Hardware event injection for validation and demonstration
Pi 4 = Edge Brain
Central intelligence, fusion engine, inference runtime, persistent store
Pi 3s = Compute Nodes
Distributed processing, mesh relay, local decision redundancy
ESP32 = Field Interface
Sensor acquisition, noise filtering, first-stage anomaly detection
Network = Nervous System
Reliable, authenticated, low-latency inter-node communication

## Slide 5
Inside One Environmental Sensor Node
Node-level architecture: from raw sensor signal to mesh-transmitted intelligence.
Sampling
Feature Extraction
Transmission
Fire Detection Node — MVP
MQ-2 smoke sensor: Analog input, 0–1023 ADC range
DHT22 temperature: ±0.5°C accuracy, 1–5 Hz sampling
DHT22 humidity: ±2% RH, cross-sensitivity correction
Air Quality Node — Future
PMS5003 particulate: PM2.5/PM10 in µg/m³
MQ-135 gas: CO₂, NH₃, NOₓ proxy
DHT22: Temperature & humidity context
Sampling & Feature Parameters
Rate: 1–10 Hz per sensor
Window: 30–60 second rolling buffers
Features: Mean, variance, rate-of-change, peak detection
Critical Design Principle: No Single Sensor Is Trusted Independently
Inexpensive sensors suffer from drift, cross-sensitivity, and environmental interference. All classification decisions require multi-sensor agreement before confidence escalates.
Sensor Pattern | Interpretation | Confidence Level
Smoke ↑ + Temp ↑ + Humidity ↓ | Strong fire signature | HIGH — escalate immediately
Smoke ↑ + Temp normal + Humidity normal | Possible local false positive | MEDIUM — flag for investigation
Smoke ↑ + Neighbor nodes agree | Spatial correlation confirms hazard | HIGH — hazard confirmed
Single sensor spike, no corroboration | Sensor drift or environmental noise | LOW — log, do not alert

## Slide 6
Mesh Networking + MQTT Telemetry Pipeline
Reliable, low-latency data transport from distributed nodes to edge gateway. Protocol stack engineered for partial connectivity, packet loss, and offline-first operation.
Example Telemetry Packet (JSON over MQTT)
{
"node_id": "fire_node_A",
"timestamp": "2026-02-15T14:32:45Z",
"sensor_type":"smoke",
"value": 0.42,
"unit": "normalized",
"confidence": 0.95,
"alert_level":"GREEN",
"rssi": -65
}
Identical packet schema used by both real sensors and the software simulator — validating the full pipeline regardless of transducer source.
Transport Protocol Stack
Layer | Technology
Physical / RF | LoRa / Zigbee / Wi-Fi 802.11
Network | Mesh topology, multi-hop routing
Transport | TCP / UDP with TLS
Messaging | MQTT v3.1.1 (Mosquitto broker)
Payload | JSON + CRC32 checksum
QoS | QoS 1 (at-least-once) for alerts
Node Identity
Unique MAC-based ID per ESP32 — prevents spoofing and enables per-node fault tracking
Sequence Numbers
Monotonic packet counter — detects loss, reordering, and replay across mesh hops
CRC32 Checksums
Payload integrity verification at both node and gateway — corrupted packets discarded
Exponential Backoff
Publish retry with backoff on failure — prevents storm conditions on mesh recovery
Local Ring Buffer
ESP32 stores telemetry during mesh outage — replays on gateway reconnect, zero data loss
Edge-Local Processing
Only alerts and summarized intelligence leave the edge. Raw sensor streams remain local.
Design Principle: Only critical alerts and summarized intelligence need to leave the edge. Raw sensor streams remain local — reducing bandwidth, latency, and external dependency.

## Slide 7
Edge AI + Multi-Sensor Fusion
From raw sensor data to environmental risk assessment — entirely at the edge.
Processing Pipeline
01
Noise Filtering
Kalman filter / moving average per sensor channel
02
Feature Extraction
Mean, variance, skewness, kurtosis, rate-of-change, peak (30–60s window)
03
Sensor-Level Anomaly
Isolation Forest / Z-score per individual sensor channel
04
Multi-Sensor Fusion
Weighted Bayesian fusion across smoke, temp, humidity, gas channels
05
Spatial Correlation
Multi-node consensus — kernel density estimation for hazard mapping
06
Risk Score & Alert
Composite score → GREEN / YELLOW / RED classification & routing
Anomaly Detection Strategy by Confidence Level
Detection Level | Method | Confidence | Action
Single-node anomaly | Isolation Forest / Z-score | Low | Log, increase polling rate
Multi-sensor agreement | Weighted Bayesian fusion | Medium | YELLOW alert, local notification
Spatial correlation | Multi-node consensus | High | RED alert, CAP message generated
Feature Engineering Detail
Feature Class | Features Computed
Statistical | Mean, variance, skewness, kurtosis (30–60s rolling window)
Temporal | Rate of change, peak detection, trend direction
Cross-sensor | Smoke + temperature correlation, humidity inverse relationship
Spatial | Neighbor-node agreement score, gradient field analysis
AI Stack
TensorFlow Lite Micro: Lightweight neural networks on ESP32 (on-node, <256KB RAM)
scikit-learn: Isolation Forest, Gaussian Mixture Models on Raspberry Pi gateway
Custom Bayesian fusion: Multi-sensor confidence weighting with configurable priors
Spatial analysis: Kernel density estimation for hazard zone mapping
Critical Framing: AI is used for anomaly detection and decision support — not magical disaster prediction. The system is transparent, auditable, and designed to fail safely. No alert is issued without multi-sensor corroboration.

## Slide 8
Offline Operation, Fault Tolerance & Security
Designed to fail gracefully: degraded operation is better than silent failure. The system defines explicit degradation states for every anticipated failure mode.
Fault Degradation State Matrix
Failure Mode | System Response | Local Capability Retained
Single sensor failure | Sensor marked offline; remaining sensors used; confidence reduced proportionally | Partial — reduced confidence scoring
Single node failure | Node marked offline; neighbor data used; network topology reconfigured | Full — spatial coverage reduced
Mesh network partition | Local buffering active; local AI inference continues; sync on reconnect | Full — isolated cluster operation
Gateway failure | Nodes continue local operation; ring buffer active; full sync on gateway recovery | Node-level only — no fusion
SACHET/CAP unavailable | Local alert remains active; OLED/NeoPixel indicates; retry queue maintained | Full — local indication active
Complete network loss | OLED + NeoPixel local indication; watchdog timer; autonomous local alert | Local — hardware indication only
Security Architecture
Node Identity
Unique cryptographic ID per ESP32 — MAC address + EEPROM provisioned secret
Encrypted Transport
TLS-secured MQTT — all broker communication encrypted in transit
Message Authentication
HMAC-SHA256 on all critical alert payloads — detects tampering
Replay Protection
Sequence number validation — monotonic counter enforced at broker
Firmware Security
Signed OTA updates with rollback protection — no unsigned code execution
Access Control
MQTT ACLs per node type — sensors cannot subscribe to alert channels
Design Principle: FAIL-CLOSED
Inability to confirm safety must not silently become "safe."
Alerts remain active until explicitly cleared by a human operator or by confirmed safe-state readings from multiple sensors
Watchdog timers trigger local indication if software stack becomes unresponsive
CRC failures cause packet discard — not processing of potentially corrupted data
Node silence (no heartbeat) is treated as a fault, not as nominal operation

## Slide 9
Prototype, Validation & Zero-Budget Engineering
Honest assessment: what is real infrastructure vs. simulated transducers. Credibility requires transparency — the architecture is real; the physical transducers are software-simulated due to a ₹0 hardware budget.
✓ REAL — Fully Implemented
Raspberry Pi 4B edge gateway infrastructure
ESP32 sensor node hardware & firmware
MQTT broker (Mosquitto) & telemetry pipeline
Wireless mesh network architecture
Edge AI inference pipeline (TFLite / scikit-learn)
Multi-sensor fusion & spatial correlation algorithms
FastAPI backend & GIS dashboard
OLED status display & NeoPixel indicators
GPIO tripwire event trigger
Offline buffering & synchronization
Alert rendering & SACHET/CAP integration framework
Raspberry Pi CPU temperature (actual hardware metric)
⚠ SIMULATED — Budget Constraint (₹0)
Physical transducers unavailable. Prototype uses a software sensor simulator generating MQTT packets in identical format to real sensors — the full data pipeline is exercised regardless of transducer source.
Smoke sensor (MQ-2) → software-generated MQTT stream
PM2.5 / PM10 particulate → software-generated MQTT stream
Water level sensor → software-generated MQTT stream
Humidity sensor (DHT22) → software-generated MQTT stream
Dedicated temperature sensor → software-generated MQTT stream
The sensing transducer is simulated; the distributed intelligence architecture is real.
7-Step Validation Plan
01
Stable Baseline
Establish nominal operation across all nodes — confirm GREEN state, low variance
02
Single-Node Disturbance
Inject anomaly on one node — validate local detection and confidence scoring
03
Multi-Node Hazard Signature
Coordinated anomaly across 3+ nodes — validate spatial correlation and RED alert escalation
04
False-Positive Injection
Noise and drift patterns — validate that single-sensor spikes do not trigger alerts
05
Network Failure Scenarios
Mesh partition, gateway loss — validate local buffering and sync-on-reconnect
06
Node Failure & Recovery
Offline → online transition — validate ring-buffer replay and topology reconfiguration
07
Alert Integration Test
End-to-end SACHET/CAP message generation — validate protocol compliance
Target Performance Metrics
Metric | Target
Detection latency | < 60 seconds
False-positive rate | < 5% per 24h window
Packet loss (mesh) | < 2%
System uptime | > 99%
Fusion accuracy | > 90%

## Slide 10
Deployment, Scalability & Technical Differentiation
From prototype to national-scale environmental intelligence layer.
Deployment Evolution
4 Nodes — Prototype
Single-cluster validation. Current stage. Core pipeline proven.
20–50 Nodes — Local Pilot
Village / ward deployment. LoRa mesh. Solar-powered field nodes.
100+ Nodes — City / Forest
Multi-cluster hierarchy. Regional edge gateways. GIS risk maps.
1000+ Nodes — Multi-Region
National-scale layer. SACHET/CAP live integration. Qualcomm silicon.
Production Hardware Evolution
Phase | Hardware | Power | Connectivity
Prototype | ESP32 + Raspberry Pi | Mains | Wi-Fi mesh
Pilot | Low-power field MCU + Pi | Solar + battery | LoRa mesh
Production | Qualcomm Snapdragon / Dragonwing-class edge | Solar + supercapacitor | 5G / LoRa hybrid
Technical Differentiation Matrix
Capability | Typical Approach | Our Architecture
Local sensing density | Limited / sparse | Distributed dense network
Edge AI | Cloud-dependent / absent | Core architecture
Multi-sensor fusion | Rare — single-sensor trust | Core capability — Bayesian
Spatial correlation | Rare / absent | Core capability — multi-node
Offline operation | Weak / limited | Built-in, fully autonomous
Alert integration | Standalone application | SACHET/CAP architectural target
Scalability model | Centralized bottleneck | Hierarchical edge-native
We are not replacing India's centralized environmental monitoring. We are adding the missing local, real-time, edge-intelligent sensing layer that operates continuously between centralized monitoring cycles — providing the village-level ground truth that satellite and centralized systems cannot.